## Slide 1: YARP
Yet Another Robot Platform

## Slide 2: Summary
What is YARP?
Who uses YARP?
How to use it?
And … Why?

## Slide 3: Let’s start from the end – Why?

## Slide 4: Why do we need a framework?
  Various scenarios and platforms
  Hardware changes in time
  Lots of different sensors
  Lack of standards
  Distributed processing
  Real-time friendly
  Algorithms/libraries/code changes in time
  Inherent complexity
  Distributed development
  Short life span of projects
HARDWARE
SOFTWARE
MAINTAINCE

## Slide 5
“If data is the bloodstream of your robot, then YARP is the circulatory system.”
[Paul Fitzpatrick]
What is YARP?

## Slide 6
“We're not out for world domination.”
[Paul Fitzpatrick]
What is YARP?

## Slide 7
YARP is a middleware aimed to ease the development of high level application for robots with a strong focus on modularity, code re-usage, flexibility and hw/sw abstraction.
Homogeneous set of libraries, GUIs, tools,
debug and run facilities
What is YARP?

## Slide 8
YARP is a middleware aimed to ease the development of high level application for robots with a strong focus on modularity, code re-usage, flexibility and hw/sw abstraction.
What is YARP?
YARP has been designed to support building robot control systems as collection of executables communicating in a peer-to-peer way, with an extensible types of connections (tcp, udp, multicast, local, MPI, mjpg, XML/RPC, tcpros, ...).
The strategic goal of this kind of design is to increase the longevity of robot software projects.

## Slide 9: Typical application
Real robot
Simulator
: Process
: Machine

## Slide 10: Who uses YARP

## Slide 11: Ports: How YARP communicates
Control
module
Port
YARP module
Vision
algoritmhs
Port
Robot
Port
Port
Image
viewer
Port
udp
mjpeg
udp
Port
Port
tcp
YARP ports are the communication entry point.
A port is a bi-directional communication entity.
Many clients can connect to a port.
Each connection can use different protocols or custom carrier to manipulate data on the fly.

## Slide 12: Ports: How YARP communicates
YARP server acts as a DNS, resolving yarp port names into system sockets
YARP module
vision
algorithms
/vision:i
Camera
/image:o
image
viewer
/view:i
udp
mjpeg
yarp server
yarp connect <source> <receiver> <carrier>(tcp)
/rpc
/command
tcp
$ yarp name list
/image:o 192.168.1.1:10001
/vision:i 192.168.1.2:10002
/view:i 192.168.1.3:10003
/command 192.168.1.2:10004
/rpc 192.168.1.3:10005
$ yarp connect /command /rpc
$ yarp connect /image:o /vision:i udp
$ yarp connect /image:o /view:i mjpeg

## Slide 13: Data types
Data in YARP are Portable classes with read and write capabilities.
class MyData : public yarp::os::Portable
{
// Portable interface toward YARP
read(…);
write(…);
// Custom user methods for data handling
fill_me();
getData();
// Usually for readability
toString();
}

## Slide 14: yarp::os::Value
Data can be extracted in its native format with asXXX function.
class yarp::os::Value : public Portable
{
Value(int x); // Create an integer data.
Value(double x); // Create a floating point data.
Value(ConstString &str); // Create a string data.
Value(void *data, int len); // Create a binary data.
bool isInt();
bool isDouble();
bool isString();
bool isBlob();
int asInt(); // Get integer value.
double asDouble(); // Get floating point value.
ConstString asString(); // Get string value.
char* asBlob(); // Get binary data value.
…
}
Value is a container able to store in a uniform way a single instance of different basic data types.
Value can be queried to know its data type.

## Slide 15: yarp::os::Property
Property prop;
prop.clear();
prop.put(“myInt”, 5);
prop.put(“myString”, “Hello World”);
prop.put(“myPi”, 3.14);
Property &myGroup = prop.addGroup(“group1”);
group1.put(“g1”, 2.5);
group1.put(“g2”, “We have cookies”);
prop.check(“myInt”);
Value myInt = prop.find(“myInt”);
double myPi = prop.find(“myPi”).asDouble();
Bottle &group = prop.findGroup(“myGroup”)
Entry can be grouped together, with a key
Works in pair <key, data>, where
Key is a string
Data is a yarp::os::Value
Entry and group can be searched by the key
Dictionary type of data

## Slide 16: yarp::os::Bottle
Bottle bot;
void clear();
bot.addInt(5);
bot.addString("hello");
Bottle& b1 = addList();
b1.addDouble(10.2);
Property &prop = bot.addDict();
prop.put(“pib”, “Help me”);
Value &v0 = bot.get(0);
Value &v1 = bot.get(1);
Can hold variable number of Value.
Most flexible type of data.
Bottle can be appended or nested one into another.
A Property can be an element of a Bottle
Bottle can be accessed using indexes.
Size is the number of element you can get()

## Slide 17: yarp::sig::ImageOf<PixelType>
Container for image type
Template working with many different pixel types
Full documentation here: http://www.yarp.it/classyarp_1_1sig_1_1ImageOf.html
ImageOf<PixelRgb> yarpImage;
yarpImage.resize(300,200);
PixelRgb rgb;
rgb = yarpImage.pixel(10, 20);

## Slide 18: Working with Ports – Client/Server
Ports are identified by their name.
Constraints:
Names must be unique
Names must start with ‘/’ character
No ‘@’ character allowed
Ideal for client/server pattern
yarp::os::Port myPort;
myPort.open(“/port”);
Bottle b;
port.read(b);
int n = b.get(0).asInt();
n++;
b.clear();
b.addInt(n);
myPort.write(b);
myPort.close();

## Slide 19: Working with Ports -- Streaming
In case of continuously broadcasted data (e.g. video streaming), a yarp::os::BufferedPort<T> can be used.
Main differences:
Data type is fixed for port lifetime
Memory creation/destruction is handled by the port
Buffering policy can be set (default latest message is kept)
A dedicated thread handles the read/write operations optimizing user thread cycle
BufferedPort<Bottle> port;
port.open("/out");
// Get memory to write into.
Bottle& b = port.prepare();
b.clear();
b.addString(“Hello world”);
port.write();

## Slide 20: Hardware abstraction
Client & Server on the same machine
YARP ports
user application
Interface
Interface
Server Network Wrapper
Client Network
Wrapper
iCub
motor controller
Simulator
motor controller
R1
motor controller

## Slide 21: Hardware abstraction
user application
Interface
Client & Server on the same machine
iCub
motor controller
Simulator
motor controller
R1
motor controller

## Slide 22: Interfaces
A class with pure virtual methods.
Servers provide functionalities by implementing required methods.
Clients use the functionalities by calling provided methods.
IPositionControl::getAxes() = 0;
IPositionControl::positionMove(…) = 0;
IPositionControl::relativeMove(…) = 0;
IPositionControl::checkMotionDone(…) = 0;
IPositionControl::setRefSpeed(…) = 0;
IPositionControl::setRefAcceleration(…) = 0;
IPositionControl::getRefSpeed(…) = 0;
IPositionControl::getRefAcceleration(…) = 0;
IPositionControl::getTargetPosition(…) = 0;
IPositionControl::stop(…) = 0;

## Slide 23: Opening a device
Devices are opened by mean of a special class called “PolyDriver”.
PolyDriver is a polymorphic class which can turn into any device.
Keyword “device” tell YARP which device we really want to open.
All other parameters will be propagated to the specified device.
PolyDriver mystica;
Property config;
config.put(“device”, “device_type”);
config.put(“deviceParam1”, paramValue1);
config.put(“deviceParam2”, paramValue2);
...
mystica.open(config);

## Slide 24: Remote Control Board
Device devoted to provide remote access to the robot motor control is the “remote_controlboard”
Required parameter to configure it are:
- Remote port prefix: remote
- Local port name: local
PolyDriver poly;
Property config;
config.put(“device”, “remote_controlboard”);
config.put(“remote”, “/icub/head”);
config.put(“local”, “/<myApplication>”);
...
poly.open(config);
CONTINUE

## Slide 25
Once opened, we need to specify which interface we want to work with.
To get a specific view of the device:
create a pointer to the interface we want to use
fill it by calling the .view(…) function
In case the device does not implement that interface, the pointer will be NULL!
A device can implement more than one interface.
IPositionControl2 *posControl = NULL;
poly.view(posControl);
if(!posControl) // handle error
...
posControl->getAxes(…);
posControl->positionMove(…);
IVelocityControl2 *velControl = NULL;
poly.view(velControl);
velControl->velocityMove(…);
Remote Control Board

## Slide 26: IPositionControl2
Give access to main position control commands.
Used to send high level targets, with a velocity & acceleration profile.
For getters, memory must be allocated by user.
Units in YARP are SI compliant, except angles for controlboard, which are in degrees, degrees/s

## Slide 27: IPositionControl2
int joints;
posControl->getAxes(&joints); // Get number of joints
posControl->setRefSpeed(0, 5); // set a speed of 5 degrees/s for joint 0
posControl->positionMove(0, 30); // move the joint 0 to +30 degrees
bool done = false;
do
{
checkMotionDone(&done); // this function checks the movement completion
}
while(!done);
posControl->positionMove(0, 0); // reset joint position to 0

## Slide 28: Other YARP features
Resource finder
Threads, Modules
Plugin loader
Carriers: mjpeg, h264, portmonitor, shared memory, depth Image, ROS
yarpView, yarpScope, Logger, MotorGui
YarpManager, YarpViz
Thrift
robotInterface

## Slide 29: Other middleware
Cool!
“But I think ROS is better”

## Slide 30
Ports can be typed or not
Multi-platform (also mobile)
Run-time reconfiguration of connections
Different carriers, user custom
QoS, channel prioritization
Smaller community
Rich set of libraries ad tools
Packages for all supported distributions
We have cookies
Both topic and service are strongly typed
Ubuntu only (ROS2 Win & Mac)
Connections from a topic use the same protocol
No concept of carrier (DDS on ROS2)
QoS on ROS2
Huge and very active community
Much more rich set of libraries and tools
Packet management
Eat children

## Slide 31: YARP - ROS carrier
YARP ask roscore to establish a new connection
YARP loads a specific carrier to convert data into ROS-like type on the fly
No need to have ROS installed
YARP module
ROS
node
yarp
node
yarp server
/topic@/yarpNode
/port
/topic
roscore

## Slide 32: THANKS FOR THE ATTENTION!